## Slide 1: Pavement Maintenance and Microsurfacing
Board of Aldermen Discussion Session
January 26, 2010

## Slide 2: Pavement Maintenance Program
Asphalt Streets (entire subdivision)
  Year 0-Asphalt Surface Installed
  Year 7-Microsurfacing
  Year 14-Microsurfacing
  Year 20-Mill and Asphalt Overlay
  Cracksealing every 2 years (east/west)

## Slide 3: Pavement Maintenance Program
Concrete Streets and Alleys
  Surface treatment on Carondelet Plaza in 2012
  Replacement of Alleys every 25-30 years
  Cracksealing every 2 years (east/west)

## Slide 4: Annual Pavement Evaluation
Performed in January each year
Each street/alley evaluated
Alley replacement prioritized based upon condition and budget
Streets follow predictable decline and improvement due to our program

## Slide 5: Pavement Condition Index
5: “Like New” condition
4: Minor reflective cracks
3: More extensive cracking, microsurfacing starting to deteriorate
2: Significant cracking. Significant deterioration of microsurfacing, leaving up to 50% exposed asphalt. Asphalt may be raveling.
1: Significant cracking, potholes forming. Nearly all microsurfacing gone. In dire need of rehabilitation.

## Slide 6: Pavement Condition Index
Scorecard goal: 85% of streets (by area) score 3 or better
  2007: 83%
  2008: 90%
  2009: 72%
  2010: 88% PROJECTED

## Slide 7: Deterioration of Pavement

## Slide 8: Reactive Pavement Strategy
Reconstruct

## Slide 9: Reactive Pavement Strategy
Reconstruct

## Slide 10: Proactive Maintenance Strategy Years 0-7
Microsurface

## Slide 11: Proactive Maintenance Strategy Years 7-14
Microsurface
Microsurface

## Slide 12: Proactive Maintenance Strategy Years 14-20
Microsurface
Microsurface
Mill & Overlay

## Slide 13: Proactive Maintenance Strategy Years 20+
Microsurface
Microsurface
Mill & Overlay

## Slide 14: Proactive vs. Reactive

## Slide 15: Benefits of a Proactive Program
Pavement maintained at higher level
Significant cost savings
Entire subdivisions treated at same time
Establishment of sequence
More predictable budget
Environmentally friendly

## Slide 16: Microsurfacing
Thin layer, approximately ¼” thick
  Residential: 1 coat
  Arterial: 2 coats
Asphalt emulsion
Water
Aggregate (granite and/or slag)
Portland Cement
Polymer Binder

## Slide 17: Microsurfacing

## Slide 18: Microsurfacing

## Slide 19: Microsurfacing

## Slide 20: Microsurfacing

## Slide 21: Microsurfacing

## Slide 22: Microsurfacing

## Slide 23: 2010 Microsurfacing Project
Residential
  1 coat (medium-duty treatment)
  Clayshire, Country Club Estates, Hillcrest
  Wednesdays, Thursdays, and Fridays
Central Business District
  2 coats (heavy-duty treatment)
  Saturdays and Sundays

## Slide 24
SUNDAY | MONDAY | TUESDAY | WEDNESDAY | THURSDAY | FRIDAY | SATURDAY
 |  | 1 | 2 | 3 | 4 | 5
6 | 7 | 8 | 9 | 10 | 11 | 12
13 | 14 | 15 | 16 | 17 | 18 | 19
20 | 21 | 22 | 23 | 24 | 25 | 26
27 | 28 | 29 | 30 |  |  | 
Project Schedule-June 2010
RESIDENTIAL
CBD
CBD
Notes: 24

## Slide 28: 2010 Microsurfacing Project

## Slide 29: Project Communications
Chamber of Commerce
Mailings
City Website
CityViews
Electronic Message Panels
Metro (bus re-routing at Transit Center)
No Parking Signage
Construction Signage

## Slide 30: Questions
Steve Meyer
Civil Engineer
290-8547
smeyer@ci.clayton.mo.us